## Slide 1
Managing Network Printers and Print Spoolers
Patrick Powell
papowell@astart.com
Astart Technologies
9475 Chesapeake Dr., Suite D
San Diego, CA 92123
619-874-6543
Copyright 1997 Patrick Powell

## Slide 2
Part 1 - Overview
Printer Connections
Printer Page Description Languages
Printer Job Languages
Print Spooler Basics
Print Spooler Structure
  BSD, SVR4, Novell, MS
RFC1179
LPRng and BSD Print Spooler Clients
  lpr, lprm, lpq, lpc
Managing LPRng/BSD Print Spoolers
  queues, starting, stopping, enable, disable

## Slide 3
Part 1 - Overview (Continued)
Setting up LPRng
  source, compilation
Printcap Files
  format, names, aliases, values
Simple Printer Setup
Filters
Complex Setup
Remote Printers
Security

## Slide 4
Part 2 - Overview
Network Print Spooling
Basic Concepts
PC View of Printing
Drivers and Print Spoolers
Printer Gateways
Microsoft Print Spooler
Windows 95 Wslpr

## Slide 5
Part 2 - Overview (Continued)
NT LPR Support
Novell Print Spooler
SNMP
Help
Summary
Q&A

## Slide 6
Part 2 - Overview (Continued)
PCNFS (Sun Microsystems)
PCNFSD LPR Support
Samba
Samba LPR Support
Desperate Measures
  LPserver and WLPserver
  WSPLR
Security
Accounting
Summary

## Slide 7
References
PostScript Tutorial and Cookbook, Adobe Systems, Addison-Wesley 1985
PostScript Language Program Design, Adobe Systems, Addison-Wesley 1985
PostScript Language Reference Manual, 2nd Edition, Adobe Systems, Inc. Addison-Wesley, 1990
Portable Document Format Reference Manual, Adobe Systems, Inc. Addison-Wesley, 1993
Web Site for Adobe and more documents:
http://www.adobe.com/supportservice/devrelations/technotes.html

## Slide 8
Software
LPRng ftp site: unless otherwise indicated, all software can be obtained from the ftp://ftp.astart.com/LPRng site. See the README and INDEX file
GNU software can be obtained from many mirror sites. Try ftp://ftp.uu.net/pub/gnu and look for MIRRORS
PostScript Utilities psutil31.tgz
More PostScript Utilities psutilmore2.tgz
GhostScript GNU
GhostView GNU
Adobe Acrobat PDF viewer/tools www.adobe.com
LPRng LPRng distribution
FILTERS_LPRng collection of filters, patched for LPRng

## Slide 9
Printer Hardware

## Slide 10
Basic Printer Operation
A Printer is a peripheral device, usually attached to a host computer
The host computer transfer print files to the printer over the communication channel

## Slide 11
Printer Communication Channels
Printer must be connected to source of print jobs
Channel determines the rate at which text (characters) are delivered to printer
Also determines the reliability
Also determines the availability of error messages and diagnostics
Simple and Cheap is not always best

## Slide 12
Serial Port
Slowest and most error prone
Older printers had a very slow transfer speed (9600 bits/second) due to the real time requirements of handling paper
Newer ones can go up to 115 Kbps
Data transmissions errors VERY common
Printer does not have a large buffer to store input so flow control is absolutely required
Hardware (RTS/CTS) flow control almost mandatory
Software flow control (DCON/DCOFF or CTRL-S/CTRL-Q) can be used over networks
Watch out for buffering in network!

## Slide 13
Advantages of Serial Port
Error and Status messages available from printer
Most systems have multiple serial ports, can attach multiple printers
Can be put on terminal server (watch out for flow control, enable RTS/CTS)
Cables can be up to 50 feet long
Cheat and they can be up to 200 feet long

## Slide 14
Disadvantages of Serial Port
Very very slow
Did I mention flow control problems? This is a major headache
Errors in data transmissions can have interesting effects
Note: Software Flow Control Headaches
  Some software flow control tries to accommodate errors by restarting transmission when ANY character is received from the other end after a time-out period.
  When you get a printer error, the printer sends CTRL-S to stop job and then later reports status, you lose rest of job. (Headache #27)

## Slide 15
Parallel Port - Advantages
Transfers data 8 bits at a time
Flow control implicit because it uses a hardware handshake for data transfer.
Very low error rate on data transfer

## Slide 16
Parallel Port - Disadvantages
Has limited bi-directional capability
  Out of Paper, Error indication
Bi-directional support limited on most interfaces
  May not be able to indicate error condition when flow control enabled
Surprisingly low throughput due to interrupt per byte on most PCs and workstations
  Games played at OS level to improve this
Real pain is getting status back using bi-directional mode
Real cheap folks can even use print sharing boxes
  You get what you pay for
  Don’t call me when they lock up

## Slide 17
Network Interface
Usually supports various protocols
  IPX (Novell and Microsoft)
  NETBUI (Microsoft)
  TCP/IP (LPD + RAW Connection)
Printer builders are (or did not use to be) network aware
Has changed tremendously over last couple of years
Configuration of interface is now usually pretty simple once you understand the various options
Front panel configuration is really quite simple
HP Jetdirect has BOOTP/DHCP configuration

## Slide 18
Network Disadvantages
Anybody can print on the printer
  Leads to the mysterious print job de jour
In spite of being on the network, only one person can actively use the printer at a time
Multiple users can/will/have locked up the interface (this is a known problem with HP Jetdirect interfaces)
Multiple users trying different protocols can/will/have locked up the interface
When the printer dies there is usually no handy way to reset it without powering it down

## Slide 19
Network Advantages
Very high throughput, and has built in flow control
Very low transfer error rate
  Ethernet has CRC
  Higher level protocols also do checksums
Can be configured using BOOTP/DHCP
Status can be obtained by using SMTP on most systems
  If DHCP working, can even reboot printer
Printer sharing becomes very simple, in principle
For shared system resource, may actually be the cheapest interface as it does not require host for support (see LPR/LPD later for details)

## Slide 20
Hybrid Solutions
Print Server Boxes
  Has network interface, supports parallel port and serial ports for printers and/or modems
  I have used several different ones with various levels of success
    Lantronics - works, configuration tricky, good functionality
    Rose - works, configuration simple, limited functionality
Dumb Network Interface (LPserver UNIX/NT/W95)
  Extremely stupid program that turns your PC into a TCP/IP raw socket connection to the printers serial (bi-directional) or parallel (unidirectional) port
  This has its place when doing accounting, very tricky printer operations

## Slide 21
HP Jetdirect Configuration
Similar in principle to most printer network interfaces
Front Panel Configuration
  Enable basic network protocols
    IPX/Novell Print Spooler
    DCP/Microsoft
    TCP/IP
      Set IP address, netmask, syslog server
    Enable BOOTP/DHCP configuration
BOOTP/DHCP Configuration
  BOOTP/DHCP supplies IP configuration information
  Specifies a TFTP server and file that has detailed printer configuration information

## Slide 22
Jetdirect Configuration File
# Administration Info
name: picasso
location: 1st floor, south wall
contact: Phil, ext 1234
# Only allow connections from network/netmask or host
allow: 10.0.0.0 255.0.0.0
allow: 15.1.2.3
idle-timeout: 120
syslog-facility: local2
# SNMP Configuration
get-community-name: blue
set-community-name: yellow
trap-community-name: red
trap-dest: 15.1.2.3
trap-dest: 15.2.3.4
authentication-trap: on

## Slide 23
Jetdirect Restrictions
The “allow” configuration parameter enables you to restrict access to the printer from the specified network/subnetmask addresses
This is essential to controlling access to your printer
You need to use the BOOTP/DHCP to set the IP address, gateway, and syslog server
Note: Setting up the BOOTP/DHCP server can be tricky. You will need to either have a DHCP server on each subnet, run a ‘forwarder’ process on a host on the subnet, or have your router forward requests to a server. (Hint: if you have Cisco router, use the “ip helper” command to specify the DHCP server address.)

## Slide 24
Direct Connections
TCP/IP Port 9100 on the Jetdirect card is a direct connection to the print engine
This is a bi-directional connection, and error messages will be written on it
Other network support cards have similar facilities; if they do not, then DON’T USE THE CARD
Usually only one connection at a time can be active; this can cause problems if trying to share the printer among several different hosts

## Slide 25
SNMP
Simple Network Management Protocol provides a common interface to obtaining information about the status of network devices.
An “agent” process resides in the network device, spies on the activities of the device, and provides information when queried.
Agents can also generate messages (traps) when a specific activity is detected
A “manager” process queries agents for status
Agents can also “write” information to the network device when requested by a manager. This allows configuration management to be done by a manager.

## Slide 26
SNMP To The Rescue (Maybe)
The SNMP standards include a Printer MIB
In principle, you can use a simple SNMP manager to query the values of the Printer MIB. These are, to put it mildly, very basic.
In practice, most vendors have extended the MIB to provide more detailed information about the error conditions, status, etc.....
Unfortunately, most print spoolers do not use the SNMP facilities to query printers
The common SNMP managers such as HP Openlook, SunNetManager, etc..... have the common printer MIBs already provided.
If you are an administrator, please learn more about managers

## Slide 27
Print Job Formats and Page Description Languages OR What Do You Send To The Printer?

## Slide 28
Print Job Data Formats
Coherent and organized approach to this subject is impossible due to historical development
Will give a rapid functional, biased, opinionated, subjective, etc.... etc... view of the subject
Remember: each manufacturer tries to distinguish their product in the market
Remember: THERE ARE NO STANDARDS
  Actually, this is a lie. There are standards. Nobody follows them :-)
Remember: The printer with the largest market share becomes the standard
Thus: Every 3 years there is a new standard.

## Slide 29
Vintage Printers (Impact, Daisy, etc...)
Fixed size characters (Fixed width/height fonts)
Character set at the whim/market demand of the manufacturers
Page dimensions based on paper sizes
  8.5 x 11 inches (letter), 11 x 15 (computer listing)
  some larger size (legal)
  whacko A4/A3 sizes (Europe)
De Facto Standard
  132 columns and 66 lines
  Unless it was 60 lines (margin at top? bottom)
  Or 80 columns with 66 line???
  And don’t forget, they change over time...

## Slide 30
Printing Text on Antiques
Send characters, print characters. Simple? Wrong.
  You forgot about INTERNATIONALIZATION
  $ ¡ are simple, try typesetting French, etc....
How about EBCDIIC? (Don’t laugh)
Tabs? Support for tabs? Why?
  Shorter jobs
  Harder to change to other manufacturer
  De Facto: tabs are at 8 positions
Market forces demand features
  Italics, true bolds, Condensed Fonts
  Need to have escape sequences to enable these
  There ARE NO STANDARDS

## Slide 31
Advice on Antiques
There are a lot of them out there - they were built for abuse, they run and run and run
Get the manuals, make 3 copies, and save them for the next generations - they will probably still be in use
Most new impact printers are extremely simple to use
  Very few features
  Modeled on major (antique) market dominators
If you have to print multiple copies on forms, this is your ONLY choice, so make sure you choose wisely
Daisy wheels make best multiple copy impressions
Dot matrix are faster, wear out
Keep a spare in the back room for parts

## Slide 32
Plotters
OK, these are not printers, but they turned out to inspire the next step in Page Description Languages
Original plotters were Analog, hooked to instrumentation.
  Drew nice curves on EXPENSIVE green paper
Market developed for plotters which could be attached to ‘smart instruments’ or computers which simulated analog plotters
  Drew backgrounds, labels, etc...
HP (and others) developed several Plotter Control Languages
  Had embedded commands for drawing text

## Slide 33
Raster Output Devices
Originally electrostatic plotters, would draw a plot a line at a time
Needed to convert Gerber (or HP or IBM…) plotter stuff to raster format
Insight that they could also produce hard copy of text using various fonts
TROFF meets VARIAN to produce $$$ of revenue as graduate students burn up 100s of rolls of expensive electrostatic paper

## Slide 34
Xerography
Xerography works by whacking charges onto a drum
The whacking is done by high intensity light
Generated by scanning original mechanically
OR BY SHINING A LASER ONTO THE PAPER AND TURNING THE LIGHT ON AND OFF UNDER COMPUTER CONTROL
VOILA!
The Laser Printer

## Slide 35
PostScript Origins
Developed originally as part of 1975-1980 research into computer graphics
Origins in computer picture generation
Text, fonts, etc..., were wedged into the language, trying to import concepts of typography into the programming language
Model used was to have dumb programs generate PostScript, and have a smart PostScript converter do rasterization
Adobe produced first PostScript Language definition, and the first PostScript printers

## Slide 36
PostScript Description
PostScript is a Stack Based Programming Language
You don’t want to know. You REALLY don’t want to know.
If you want to know, you are warped. Or a Computer Science Whacko.
PostScript files are programs.
A typesetting program is a Program Generator that produces programs for another computer that runs to produce your output.
Are you starting to understand why you have problems with printing PostScript?

## Slide 37
PostScript Printer Control
Since PostScript is a program running on the printer, why not give it the ability to control the type of paper, paper trays to be used, duplex printing, etc...?
We do this by having the PostScript program set values of various system dictionary variables (I told you, you REALLY don’t want to know).
After the job finishes, you should really revert to a known state of these system dictionary variables
Right? Wrong! You may want to set these to be permanent for all jobs
So we have a password needed. Guess what the password is? Right. You guessed it! (Answer: no password)

## Slide 38
PostScript Disadvantages
Since it is a programming language, it comes in different versions
  This is mandatory, and is Bernard’s Law: Never trust Version 1.
It requires memory to store the program, to hold temporary results, and to do rasterization, font conversions, etc....
  Thus we encounter Booth’s Law: You never have enough memory for a graphics program.
There is always a bug in the compiler/interpreter
  Even correct PostScript code does not always work.

## Slide 39
PostScript Disadvantages (Cont’d)
Since you are running a program, the page generation can be hideously slow if you are doing fancy graphics operations such as scaling, rotation, etc... of large bit mapped graphics and fills
When a problem is encountered, you have limited diagnostic capability.
Ghostscript Is Your Friend - Use It

## Slide 40
PostScript Advantages
Incredibly portable across different vendors’ printers
Not due to the language, but due to Adobe selling the code for the Interpreter at such a low price that everybody used it (Not true any more, so we are seeing some interesting PostScript bugs).
Now everybody needs to be Adobe Bug Compatible
  Remember: THERE ARE NO STANDARDS
Previewers can be built that will give you an exact idea of what your PostScript will look like
De Facto the standard, most portable way to generate documents for printing

## Slide 41
PostScript Books
PostScript Tutorial and Cookbook
  The Blue Book
  Very easy to read
  Use Ghostscript and learn about PostScript programming
PostScript Language Reference Manual
  2nd Edition
  Almost incomprehensible; it IS a standard, after all
  Appendixes are VERY helpful
  You can get a copy from Adobe’s web site
www.adobe.com

## Slide 42
Embedded PostScript (EPS)
Self contained PostScript files that produce a graphical object when executed
See PostScript Reference Manual Appendix H
  Version 3.0 is most common
  Almost all graphical object editors import and/or export EPS
  Some Web browsers even have extensions that display it

## Slide 43
PostScript Document Structuring Conventions
PostScript Reference Manual, Appendix G
  Version 3 is most generally used
Specifies how PostScript should be used for document generation
  Prologue sets up overall characteristics of document, such as fonts, subroutines, etc...
  Body consists of set of independent pages
  Each page can be removed/duplicated/inserted in document without altering printing
  Standard also provides guidelines for information about document

## Slide 44
Tools For PostScript
Assumes Document Structure Version 3
PS Utilities Version 3.1 (psutil3.tar.gz)
  Set of UNIX tools for massaging PostScript file
  psnup will print N virtual pages per real page
  psselect will select pages to be printed
  psrev will reverse page order
PS fixer (psmoreutils2.tar.gz)
  merges pages of two documents, good for putting a background on a document
  Selectively places/orients individual pages or sets of pages on a document
  desperation tool made from psutils, cannot live without it

## Slide 45
Tools for PostScript (Cont’d)
Several tools available that allow you to add documentation control to PostScript files
  For example, you can have the first page fed from a special tray, and then remainder from another tray
  These are usually commercially available, but freeware/shareware versions have been spotted.
  Some commercial print spoolers incorporate this functionality into their Print Spooler filters (see later)
See the LPRng ftp/web site for pointers

## Slide 46
Binary Communications Protocol
PostScript language specification states that the program must be in printable ASCII characters or a limited set of control characters
However, you can embed inline binary data into a PostScript file using very tricky methods
Some control characters normally cause a PostScript Interpreter to end execution, send status, or may actually be ignored.
The Binary Communications Protocol escapes these control characters. If you have character C needing escape you send: 0x01 C ^ 0x40
  e.g. - 0x01 (^A) -> 0x01 ‘A’ or 0x01 0x41

## Slide 47
Tagged Binary Communications Protocol
Warning
  If you have a file with embedded BCP escapes and you redo the BCP escapes, then you will destroy the escaping
This leads to the Tagged BCP protocol
  We add a ^A M sequence (this is an escaped CR character) to indicate that we are doing BCP and have put in the escapes
  When we scan the file and detect ^A M we do not add more escapes
This is one of the leading causes of problems printing PostScript files with binary images produced by some graphics programs

## Slide 48
Postscript Printer Description Files (PPD)
You can use PostScript to manage and control various printer operations
  What variables/operations/values do you need?
Each PostScript printer should have a PostScript Printer Description file that contains the various PostScript manageable options and how to set them
Example: HP4MP - setting manual feed
*ManualFeed True: "1 dict dup /ManualFeed true put setpagedevice"
*ManualFeed False: "1 dict dup /ManualFeed false put setpagedevice"
The contents include the PostScript needed to set the required operations
Easy to extract from the PPD file and send to printers

## Slide 49
PPD Warnings
Each printer has a possibly different set of commands, so check the PPD file for the printers
Manufacturers are not required to provide PPD files, so you may have to dig around for them.
There are many extensions to the basic PPD capabilities, some of which are very specific to a particular printer.
WARNING: I have discovered discrepancies between the PPD, manual, and actual operation. RTFM, and try it out.
WARNING: some options interact, and will lock up printers. PPD and documents do not cover this

## Slide 50
HP PCL
Hewlett Packard developed a line of laser printers and wanted to sell them to the various printing markets
They also did not like paying Adobe royalties and licensing fees
They invented the Printer Command Language (PCL)
  Version 1, Version 2, Version 3, Version 4...
  Currently we have Version 5 and rumors of 6
PCL is NOT a programming language, it is a Printer Command Language
It specifies where on a page to draw lines, glyphs, and does it very well.

## Slide 51
PCL References
PCL 5 Printer Language Technical Reference
  Surprisingly readable, but BORING, repetitive, and written in a horribly verbose manner.
Read and memorize Section 3.8
  Resetting the Print Environment
  \]E and \]%-12345X are your friends, and will help you keep your sanity
  Note that this sequence, when sent in a PCL file, will terminate job printing and may have some surprising consequences
Read Chapter 4 - PCL Job Control Commands
  This will explain most of the printer control functions

## Slide 52
PCL Evolution
Original versions of PCL did not support downloadable fonts.
This was supposed to be a feature - you would buy font cards and plug them in.
User feedback (flames) convinced HP that they needed to support downloadable fonts
Then we had raster graphics support added
Then we had page structuring support added
It now can make the printer sing, dance, and do just about anything (as long as you know the correct PCL commands)

## Slide 53
PCL Disadvantages
Older PCL printers do not have downloadable font support
You may (again) need lots of memory for fonts, images, etc.... (There’s no such thing as a free lunch)
It uses control characters (ESC) for many of the commands, making it difficult to fix/mangle/edit PCL files without special editors capable of handling long lines, control characters, etc....

## Slide 54
PCL Advantages
Simple simple to generate
Slightly smaller files than PostScript
Very much faster page generation, as there is little to do except read the input and copy BitBlits to the graphics memory
Even has commands to do the printer mechanism commands such as bin selections, etc...., built into the language now.

## Slide 55
Mystery PCL Commands
Since each printer has a different set of capabilities, you need to have PCL commands to operate the printer
There should be a “PCL Printer Description” file for each printer, right?
  ANSWER: no
Each printer should have a document providing a complete list of the PCL commands supported, right?
  ANSWER: ummm… right… but only the development group has that information, the printer is not in development any more, …
Situation is getting better, but documentation is still weak point for specialized operations

## Slide 56
Quick Test
If you are using PostScript and TBCP, what is the end TBCP sequence?
ANSWER: \]%-12345X
If you want to make sure that your PostScript job gets printed, even if the previous job did not end with the EOJ string, what should you put into your file?
ANSWER: \]%-12345X before the PostScript
If you are trying to decide if a file is PostScript or PJL or text, you might try looking for %!PS as the first characters, right?
ANSWER: Yes, No, Maybe? Sigh… It all depends on how smart/stupid/weird the writers of the PostScript generation program are...

## Slide 57
Quick Test (Cont’d)
How can you tell if you have PCL or PostScript?
  Ummm… throw it at the printer and if it works, it was PostScript
GhostScript can be modified to disregard the various PCL sequences. This makes life much easier when trying to preview files produced on MS/Apple based programs

## Slide 58
Portable Document Format (PDF)
PDF is basically PostScript’s version of PCL
  It is very simple
  All the time consuming PostScript operations are disallowed
  There are some minor HyperText things thrown in to provide some previewer help
Concept was to generate your document in PostScript or PCL, run it through a PDF converter, and you get PDF.
To print, you expand the PDF into the more verbose PostScript, add the Job Structuring Conventions, and you are done
Adobe now sells PDF viewers and translators...

## Slide 59
Printing PDF
Very few (none?) printers will accept PDF files
You need to preprocess them into PostScript
  Ghostscript should be able to do this
  Whoops its cookies on many PDF files
  Open question

## Slide 60
Portable Job Language
Now printers have to support PCL, PostScript, TEXT, and who knows what.
Documents need to be printed using different papers, formats, orientations, etc....
Need a higher level language to control this type of operation, overriding (perhaps) the operations in the document
Portable Job Language was intended to do this
Most important feature is ^]-012345XPJL EOF
  This causes a functional reset of the printer
  Cannot be ignored, escaped, hidden, etc....
  Restores sanity to the printing world

## Slide 61
PJL Features
Provides ways to specify the Page Description Language
  PJL Select Postscript
Provides ways to specify the orientation (if the PDL does not override it)
Basically, provides a way of overriding the PDL requests
And most important:
  Provides a standard set of error messages to be returned IRREGARDLESS of the PCL
This last feature is worth the pain and effort of PJL

## Slide 62
PJL Disadvantages
Not all PJL features are supported in all printers
Printer vendors are very closed mouthed about what they support. There is no “PJL Printer Document” standard for PJL
HP does not provide details on all of the error messages, leaving it up to implementers to discover that there are a whole new set of messages concerned with various printer operations
  Try getting a paper jam in a multi-bin feed printer and see what messages you get
Different releases of printer EPROMs support different PJL sets
  HPXXSi are notoriously different from other HPs
And of course - different vendors have different messages

## Slide 63
PPD Meets PJL
If a printer supports PostScript, there is usually a PPD file for the printer.
HP has very nicely put in the various PJL and PostScript sequences needed to perform the various printer control functions in their distributed PPD files.
This information is not documented of course… but handy to know

## Slide 64
Print Spoolers

## Slide 65
Print Spooler Basics
Users create jobs (print files)
They use a print client to send job to a print server or spooler
The spooler then transfers jobs to a printer
Multiple users (clients) can transfer jobs to a server
A server can transfer multiple jobs to printers

## Slide 66
Common Print Spooler Architectures
LPR/BSD UNIX
  variants include PLP, LPRng
  RFC1179 documents client/server protocol
  TCP/IP network based
LP/SVR4 UNIX
  Proprietary client/server protocol
Novell Netware
  Semi-proprietary protocol
  IPX Network based (or IPX over TCP)
Microsoft SMB
  Basics documented, but details are not
  NetBUI, IPX based

## Slide 67
LPR (BSD/RFC1179) Architecture
lpd is the print daemon
  listens on port TCP port 515 for requests from lpr clients
  uses printcap for configuration
lprm (job removal), lpq (job status) communicate over port 515
jobs stored in spool queue on server host

## Slide 68
LP (SVR4) Architecture
lpsched is the print daemon
  listens on /dev/printer (FIFO)
  uses /etc.../lp/* files for configuration
lpstat, lpadmin, accept, enable used to control operation
jobs stored in spool queue on server host

## Slide 69
Novell Print Server Architecture
File Server is the print daemon
  files placed on server and requests made for printing from clients
  uses database for configuration
printing done by server process on file server or other host
management done using admintool or other facility
jobs stored in spool queue on file server

## Slide 70
NT Print Server Architecture
Server is the print daemon
  files placed on server and requests made for printing from clients
  uses registry for configuration
printing done by server process on file server or other host
management done using control panel
jobs stored in spool queue on file server

## Slide 71
Observation
Architectures are almost identical
Should be easy to understand, right?
  WRONG
You can set up the various pieces easily, but the problems start when you want to do more than just fling files at printers
  Accounting
  Restricting access
  Error logging and recovery

## Slide 72
RFC 1179 Line Printer Daemon Protocol

## Slide 73
RFC1179
Documented the original BSD print spooler client server protocol
Incomplete, inconsistent, and open to abuse
Only common, non-proprietary, open standard available today
  This situation may change as the IETF has a Internet Printing Protocol (IPP) working group making progress towards a new and sensible standard

## Slide 74
Basic Concepts
Server listens on port 515 for connections from clients
Clients open connection from port 721 - 731 to server
Clients send servers requests, get confirmation or status
Request can be:
  (LPR) transfer job
  (LPQ) get queue status
  (LPRM) remove job
  (LPC LPRng Extensions) queue control

## Slide 75
Print Job
control file
  contains information about the job submitter and the way the job is to be processed by the print server
  names the data files for the job
one or more data files
control file and data files are transferred in binary form from client to server
  server must interpret contents of files

## Slide 76
Print Job Files
File names have defined format
  cf X nnn hostname - control file
cfA001patrick cfA002patrick.astart.com
  X is a letter indicating job priority
  nnn is a ‘job sequence number’
  hostname is the name of the host originating the job
Data file names should have same format
  df X nnn hostname
dfA001patrick dfB001patrick
  the X is a sequence identifier
Order that files should be sent in is not defined
Most network printers ignore the control files and just print data files, treating each as an independent job

## Slide 77
Control File Format
Each line provides information about the job submitter, the job options, or how the data files are to be printed
Hastart4.astart.com Host name
Proot User name (banner)
J(stdin) Job title
CA Job class
Lroot User name (billing)
fdfA458astart4.astart.com Data file
N(stdin) Data file name
UdfA458astart4.astart.com Unlink data file
Lines starting with upper case letters are information
Lines starting with lower case letters are data files

## Slide 78
Data File Format
Each data file in the control file is identified by a line starting with a lower case letter.
This letter indicates the “format” of the data file and is a hint to the server on how it should be printed.
The U lines in the control file were originally used to indicate that the spooler should remove the data files after printing. By default, most spoolers do this by default.
As you see, the format of the control files is trivial
It is amazing that so many implementations get it wrong...

## Slide 79
Job Transfer Protocol
Client sends a line of the form:
\002printer\n
Server responds with \000
Client sends control file transfer request
\002cfXnnnhostname length\n
Server responds with \000
Client sends length bytes of control file, then \000
Server responds with \000
Client sends data file transfer request
\003dfXnnnhostname length\n
Server responds with \000
Client sends length bytes of data file, then \000
Server responds with \000
Repeat sending data files until all done

## Slide 80
Protocol Headaches
Some clients decide to send data files first, then control file
Some clients do not send data files in same order as in control file
Some clients send \n\r or \r\n instead of \n
Some clients put non-ASCII or space characters in the control file
Some clients do not use correct names for data files
Some clients put in non-present data files
  Now, nobody would put in a line like:
f/etc.../password or U/etc.../password in the control file, would they? Hmm...

## Slide 81
Printer Status (LPQ)
RFC1179 uses the following protocol to get printer status
Client sends
\003printername [keys]\n short? format
\004printername [keys]\n alternate?
\009printername [keys]\n LPRng verbose
Server responds with status, then closes the connection
There is no definition of what the status format must be. Every LPD server returns a different one
Keys are used to refine the status, e.g. - select a job
No definition of what information is searched for...

## Slide 82
Remove Job (LPRM)
RFC1179 uses the following protocol to remove printer job
Client sends
\005printername user[keys]\n
Server responds with status, then closes the connection
There is no definition of what the returned status format must be. Every LPD server returns a different one
Keys are used to select a job
No definition of what information is searched for...

## Slide 83
Start Printer (LPC)
Amazingly, RFC1179 only has one command to control a printer.
Client sends
\001printername\n
Server responds with \000 and starts the printer

## Slide 84
LPC (Not Defined by RFC1179)
In addition to the standard functions defined by RFC1179, there is need for some sort of administration control.
This is not part of RFC1179, and is usually implemented by the LPC program.
Thus, there is no way to remotely manage a printer using RFC1179, leading to the use of SNMP...

## Slide 85
LPD/BSD and LPRng Print Servers

## Slide 86
Why LPD/BSD?
Uses RFC1179
All other protocols are proprietary
It is trivial to implement over a network, and allows any TCP/IP based protocol to provide print services
Other protocols can be gatewayed to RFC1179 based printers/spoolers with very little effort
Least common denominator in multiprotocol printing
Available on all UNIX, Microsoft, Apple, etc... etc... platforms

## Slide 87
Why LPRng?
LPRng is a descendant of the LPD/BSD family of spoolers
It was meant to be used in environments where you needed to exercise management control over printing operations
It has incredible flexibility, logging, debugging, etc... etc...., and allows a high degree of management control over printing, spooling, user access, etc....
You pay for this by not having a simple plug and play system
From the users viewpoint, LPRng strongly resembles the LPR/BSD print spoolers
The architecture is similar, but not identical to original BSD

## Slide 88
LPRng Supports Remote LPC
Major problem in large system administration is management of print queues
To do this, you must log in as root and run the LPC command
LPRng extends RFC1179 and provides a LPC command as well as the LPQ, LPRM, and LPR support
There is even a strongly authenticated version using Kerberos, PGP, or SSL available (compile time option).

## Slide 89
LPRng Security
One of the reasons for LPRng was trying to deal with many of the security loopholes present in the original BSD code
There are still several loopholes present in various LPR distributions, most are annoyance level, but some are very serious
Remember - LPR/BSD clients run SUID root, allowing users access
LPR/BSD runs filters as root, and some filters are shell scripts with such things as
exec $*
LPRng code takes much more care about these things

## Slide 90
LPD/BSD Details
lpd is the print daemon
  listens on port TCP port 515 for requests from lpr clients
  uses printcap for configuration
lprm (job removal), lpq (job status) communicate over port 515
jobs stored in spool queue on server host

## Slide 91
/etc.../printcap
Database used to control printer operations
Originally based on the termcap format, but has since departed radically
#parallel attached DUMB printer
pr1|dumb:\
:lp=/dev/lp:sh@:sb:mx#1000:\
:sd=/var/spool/lpd:\
:of=/usr/libexec/of:\
:if=/usr/libexec/if
The first part of the printcap is the primary (reference) name and the printer aliases.
Following entries are either keywords and values, flags (:sb: set sb flag on, :sh@: sets sh flag off), or numerical values (:mx#1000: or :fx#0x13:)

## Slide 92
Important keywords
lp = the local printing device
rm=remote host, rp=remote printer
  used when jobs are to be forwarded to another host using RFC1179 job transfer
sd=spool directory
  where the jobs are stored
sh - suppress (no) headers (banners) when printing locally
sb - short (1 line) banner instead of long one
mx # - maximum job size (0 is unlimited)

## Slide 93
Lightweight printcap files
LPRng eliminates much of the overhead of the BSD printcap files #simple printer entry lp|pr: :lp=pr@host%515 lp2:sd=/var/lpd/lp2:lp=lp2%9100 :if=/usr/libexec/hpif :of=/usr/libexec/hpof
No \ at ends of lines, use indentation instead
lp now can specify remote printer and host, as well as port
The form host%port opens a connection to a port on the remote device - allowing direct access to printer (for PJL status reporting)

## Slide 94
LPR Client
Takes a list of files, or input from STDIN, and generates a control file, transfers the control file and data files to the LPD server
BSD/LPR used to write control and data files to the spool directory, requiring SUID ROOT permissions
LPRng uses a network connection, and takes extreme precautions when reading and writing files; by default, LPRng’s LPR runs as a user program

## Slide 95
Binary, Text, and Format Files
By default, LPR assumes that files to be printed are text, and sets their format in the control file as f (as in text file)
When printing these files, the server will pass them through a filter which may modify the file; this can have disastrous effects on files containing binary data
The l (literal) format specifies that no filter be used; however too many people confused 1 and l so the -b (binary) flag is used to specify literal format
lpr -b /tmp/binaryfile
Just to make life miserable, some PC based LPR clients decided to use v format in the control file for binary files… Sigh...

## Slide 96
Lightweight Clients
The standard BSD implementation requires the printing clients to transfer jobs to a LPD server running on the local host. The local LPD server then will transfer jobs to remote hosts
LPRng implements lightweight clients, which will simply transfer jobs directly to remote hosts, eliminating the need for a server running on the local host. This also reduces file space requirements on the local host.
If the destination is a printer that implements RFC1179, then you never have to store the print files

## Slide 97
LPD/BSD Printer Specification
The LPR -Ppr option explicitly specifies the destination printer
If not specified, the PRINTER environment variable sets the default printer; if there is no PRINTER environment variable, the first one in the printcap file is used
Note that in LPD/BSD that the LPR client always transfers the job to the local LPD server, which stores it in the spool queue
This led to the horrible “set symbolic link” and “remove after printing” options which have been exploited in the past to do horrible things (but not by your users, right?).

## Slide 98
LPRng Printer Extensions
The -Ppr@host form causes LPRng to send the print job directly to the printer on the remote host
If not specified, or not a direct form as above, the PRINTER environment variable and printcap file are then used
If the printcap entry has the form lp=pr@host or has :rm:rp: information, the LPR client transfers directly
For total abuse, you can use
lpr -Phost%port/direct
This causes the client (and LPD server) to simply open a connection to the remote port and pipe the files directly to it. No filters, etc.... Very handy for lightweight printing.

## Slide 99
Filters and Job Processing
When a job is selected for printing, the LPD server examines the control file for data file format information
fdfA001astart4 format f
The printcap information is checked for a format f filter program
The data file is piped into the filter program and the output is then sent to the printer device
If the printer is connected via a simple TCP/IP connection to a port, I.e. - HP Jetdirect port 9100, then LPD/BSD requires special filters to open connection
LPRng does this using lp=host%port, simplifying things

## Slide 100
Filter Specification
Filters are specified in the printcap file as follows:
of = filter for banner printing (OF filter)
if = filter for text printing (format f) (IF filter)
Xf = filter for format X (XF filter)
If no filter is specified, then no default filter is used
The OF filter is used to print banners at start and end of job. It does nothing else.
Files with l (literal or binary format) are passed through the IF filter; however, it is invoked with the -c (clear text?) flag.
/usr/libexec/lpf -c

## Slide 101
Basic Filters - Text Transformations
A filter is given a print file on STDIN and produces output for the print device on STDOUT
The most basic filter action is to translate LF to CF/LF combinations; most antique (vintage) printers require this
Then we need to expand tabs
Then we better look for sequences of \b (backspaces) and overstrikes, and replace them with the right control sequences

## Slide 102
LPRng’s lpf filter
Extremely simple filter that will do LF to CF/LF expansion, tab expansion, and most simple printing operations such as inserting NULLS after page eject
  NULLS? yes, sometimes you need to do this to pause long enough for the printer to do a form feed… Sigh
When used as the OF filter, will expand a short banner string (single line) into a very nice full page banner
This type of thing is used less and less these days, but periodically there are requests for this antique.

## Slide 103
PostScript Printer Filters
Many times PostScript printers are used to print text files; the IF filter should detect a non-PostScript file, and invoke a Text to PostScript translator
Some printers stack paper in back to front order; the IF filter should try to do page reversal
If the destination printer has PJL support, you better insert the various PJL/PCL strings to reset the printer and put it into PostScript mode.
Did I mention getting page counts? And accounting? and storing this in an accounting file? And checking that the person has permission to print?

## Slide 104
LPRng’s psfilter
This filter tries to handle most common PostScript printer problems
  it sends reset sequences
  it gets status information and produces error messages
  it even logs messages returned during job printing, such as the PostScript emulators error messages
  it gets the value of the page counter from the printer
  It is incredibly paranoid about file formats and tries really hard to make sure that the job being sent is PostScript
  Yes, it supports Tagged Binary Communications Protocol

## Slide 105
APSFILTER
ftp://sunsite.unc.edu
/pub/Linux/system/printing/aps-491.tgz
author Andreas Klemm
andreas@knobel.gun.de
co-author Thomas Bueschgens
sledge@hammer.oche.de
Very nice package that valiantly tries to determine the format of the input files (uses UNIX file utility) and then passes them through the appropriate filters.
One of the nice features of this package is that it will even use GhostScript to produce output for a non-PostScript printer
Strongly recommended for those desperate situations where run time and file space is no object but “User Proofing” is

## Slide 106
LPRng’s CTI-ifhp Filter
Designed to handle HP printers
Totally shameless rip-off of the very good JetAdmin filter set produced for Solaris/SunOS
The wide variety of HP printers makes it difficult to have a single filter automatically handle all situations, but the ifhp filter tries hard
Various flags and options allow it to handle all known HP printers that have published PPD files with PJL information (I hope!)
Switches between PCL and Postscript, has a text to PostScript converter, and tries very hard to do duplex, etc...., control

## Slide 107
Managing Printer Operations

## Slide 108
Printers, Queues, and Status
All jobs handled by LPD are placed in a print queue, and then sent to a printer
Queue State
  enabled - accepting jobs
  disabled - not accepting jobs
Printer (Destination) State
  running - actively printing job
  idle - waiting for job to print
  stopped - administratively stopped from printing

## Slide 109
LPQ - Status
The LPQ command is used to request status about a printer or print queue status
LPD/BSD has two forms of status - short and long
LPRng adds verbose (which is REALLY verbose!)
When a LPD server gets a status request, it replies with status for the local queue, and then if the queue is forwarded to a remote printer will forward the LPQ request.
If the printer is local to the LPD server, the server will also report printer activity
You can restrict the status to only selected jobs by adding keys to the request command. These usually are the user, job id, or host from which the jobs originated.

## Slide 110
LPQ and Security
One of the major flaws in the RFC1179 protocol is that there is no way to identify the originator of a LPQ request. Thus, there is usually no restriction on the data or information returned.
Since LPQ returns the host and user which submitted a job, this is a very good way to find the names of machines and hosts to probe when doing hacking attacks
Firewalls should disable port 515 for this reason in both directions, as you do not want your folks hacking other systems, right?

## Slide 111
LPRM - Job Removal
The LPRM program generates an RFC1179 job removal request
Note that RFC1179 specifies that a user name must be supplied
In practice (I.e.. - this works folks) most LPD/BSD systems will accept any request from any system to delete a job.
The wimpy “requests must originate from port 721-731” restriction can be circumvented with a PC and a simple hacking program. Sigh…

## Slide 112
LPC - Printer Control
The LPD/BSD system usually provides a LPC program that is used to control the LPD activities. Traditionally it does this by reading and writing files in the spool queue, and changing permissions on directories
The details of this are too ugly for public discussion. You really don’t want to know.
This means that you must log onto the server as ROOT to control the print queues
You can then use the enable/disable commands to enable or disable queuing, and the stop/start commands to start or stop printing from a queue

## Slide 113
LPC - More Commands
abort - kill off the filters doing printing and don’t restart printing
  Used when a job gets hung up, the filter is unable to process it, or there is something very strange
  Job can then be removed using LPRM
up - short for enable + start
down - short for disable + abort
restart (BSD) or kill (LPRng) - kill off the filter and then restart it

## Slide 114
Print Queue Priority
This is explicitly undefined by RFC1179
Most print queues run on a first come, first serve basis
The LPC topq (top of queue) command will put the selected job at the top of the queue (You really don’t want to know how
LPRng has several extensions to priority
  Jobs are sorted by name

## Slide 115
LPRng LPC Extensions
In order to more effectively manage printers, LPRng has extended the RFC1179 protocol to allow LPC commands to be sent to the LPD server
These command can be authenticated and/or encrypted using Kerberos, PGP, or the SSL facilities
In addition to the regular LPD/BSD commands, the following commands have been added
lpc reread
  the lpd server will reread the printcap and configuration information files
lpc kill
  kills and restarts a printer. Handy for restarting printing of a job

## Slide 116
Installing and Setting Up LPRng

## Slide 117
Installing LPRng
Get the source code from a distribution site
  ftp://ftp.astart.com/pub/LPRng/
  Get the distribution (LPRng-version.tgz)
  Get the filters as well (LPRng_filters-version.tgz)
You will need ANSI C compiler, GNU Make, GNU Zip (gzip)
Uncompress and tar the distribution
gunzip -c LPRng-*.tgz |tar xf -
Configure, compile, and install the code (see documentation for details
configure; make clean all install
Install the default configuration and permissions files
make default

## Slide 118
LPRng's checkpc Program
The checkpc program reads the printcap files and checks the system spool directories for consistency with the printcap information
When invoked by root, checkpc -f will change permissions and create the required files and directories
It can also be used to remove old files and truncate log files.
See the checkpc man page for details

## Slide 119
Setting Up LPRng on BSD Systems
You must first stop the current LPD
ps -axu | grep lp get the LPD PID
kill pid
Run checkpc to fix the permissions, etc...
checkpc -f
Edit the rc.local or other rc file to start LPRng lpd
if [ -f /etc.../printcap ] ; then
echo -n ' lpd' ; /usr/local/bin/lpd;
fi;
Start lpd and test the system
lpd

## Slide 120
Setting Up LPRng on Solaris/SVR4
The default printing system on Solaris is the lp print spooler. You must first disable this, as well as the various network print services
lpshut;
nlsadmin -r lpd tcp;
nlsadmin -r lp tcp;
Check the /etc.../printcap file, then run checkpc to fix the various system files
checkpc -f
Next, modify the rc files to start lpd instead of lpsched
Reboot the system
Check the system using lpq, lpr, etc....

## Slide 121
LP System Emulation
When the various LPRng clients are invoked using the LP system names, they will emulate the lp system behavior. This can be done by making symbolic links to the various files:
ln -s lpr lp;
ln -s lprm remove;
ln -s lpq lpstat;
This allows programs which require the LP print system to directly use the LPR print facilities

## Slide 122
Printcaps and Printer Setups

## Slide 123
Simple Parallel Port Printer
# parallel port printer, no banner
lp:sh:mx#0:sd=/var/spool/lpd/lp
lp=/dev/pr
if=/usr/libexec/lpf
The sh suppresses banners, mx#0 allows unlimited size files. The printer device (/dev/pr) is opened write only by default.
The lpf filter will do LF to CF/LF translation, expand tabs, etc....
This is about as simple as you can make a printcap entry

## Slide 124
PS, PJL, or PCL Parallel Port Printer
# parallel port printer, no banner
lp:sh:mx#0:sd=/var/spool/lpd/lp
lp=/dev/pr
# For PostScript printer use psfilter package
if=/usr/libexec/psif -Tstatus=off
# For PJL, PCL printer use CTI-ifhp package
if=/usr/libexec/ifhp -Tstatus=off
The status=off flag suppresses the filter from getting printer status, as the parallel port is write only
The psif and ifhp filters will do Text to PostScript or PCL conversion, and will detect PostScript or PCL files
See the psfilter and CTI-ifhp documentation for details

## Slide 125
Simple Serial Port Printer
# serial port printer, no banner
lp:sh:mx#0:sd=/var/spool/lpd/lp
:rw:lp=/dev/ttya
:sy=9600 -echo -crmod -raw \
-oddp -evenp pass8 cbreak ixon
if=/usr/libexec/lpf
The rw flag opens the serial port read/write
The sy (stty) option sets the characteristics of the serial line
Any error messages from the printer will be passed to the LPD server for action

## Slide 126
PS, PJL, or PCL Serial Port Printer
# serial port printer, no banner
lp:sh:mx#0:sd=/var/spool/lpd/lp
:rw:lp=/dev/ttya
:sy=9600 -echo -crmod -raw \
-oddp -evenp pass8 cbreak ixon
# For PostScript printer use psfilter package
if=/usr/libexec/psif
# For PJL, PCL printer use CTI-ifhp package
if=/usr/libexec/ifhp
Since the serial port is Read/Write, the filters can query the printer for status and use this to control various operations

## Slide 127
PS, PJL, or PCL Network Port Printer
# serial port printer, no banner
lp:sh:mx#0:sd=/var/spool/lpd/lp
:rw:lp=prname%9100
# For PostScript printer use psfilter package
if=/usr/libexec/psif
# For PJL, PCL printer use CTI-ifhp package
if=/usr/libexec/ifhp
The LPD server will open a connection to port 9100 on the printer, and the filters will direct their output to this port
This is extremely effective for network based printers

## Slide 128
Printer Pools and Load Sharing
The LPRng software can do load sharing between a set of printers by having a master spool queue and a set of servers printers
The jobs in the master queue are sorted by priority and when a server printer is idle, the job will be placed in the serve printer queue
master:ss=serv1,serv2
:sd=/var/spool/lpd/master
serv1:sv=master
:sd=/var/spool/lpd:lp=/dev/pr1:...
serv2:sv=master
:sd=/var/spool/lpd:lp=/dev/pr2:…
Jobs can also be spooled directly to the server printers as well

## Slide 129
Bounce Queues and Filters
Sometimes it is necessary to perform filtering actions on jobs and then send the job to another print queue
This is common when dealing with network printers, or when you want to have special actions performed by a special queue
#do 2 pages per page up
pr2up:lp=realpr@host:if=ps2up
#real printer
realpr:lp=pr%9100:sd=/sd:if=ifhp
The pr2up printer simply passes 'f' format jobs through a 2 up (2 virtual pages/real page) filter and then sends the job to the real printer
This action is called a bounce queue

## Slide 130
Editing Control Files
A bounce queue can also be used to modify a control file. This is commonly needed when either the format of the control file is unsuitable for the destination printer, or when data file formats need to be modified as a result of filtering
prgif:lp=realpr@host:sd=/sd:rf=/gif2ps
:edit_cf=/usr/lib/cf_editor
The cf_editor filter is given the control file and can edit as well. Note that this can include actions such as removing job files.

## Slide 131
Routing
Sometimes it is necessary to dynamically decide what actual printer a job should be sent to based on information in either the control file or the format of data files
A routing filter can decide the destination of the job and the LPD server can then transfer the job to the destination
See the LPRng documentation for details of this operation

## Slide 132
Summary
The BSD/LPR print spooling system is still the most common and useful for general print spooling
It can be extended in a simple and easy to understand manner

## Slide 133
Part 2 Multi-platform Printing and Gateways

## Slide 134
Print Job Preparation
When a print job is generated, it is necessary to translate the desired information into a format suitable for the destination print engine.
There are two general approaches to the problem:
  Do the conversion as late as possible in the translation process (late binding)
  Do the conversion as early as possible in the translation process (early binding)
Late binding has the benefits of flexibility, but the actual translations possible may be limited to a few known by the destination
Early binding restricts the actual output to a known printer, but can handle a much wider variety of printable objects

## Slide 135
LP / LPD Uses Late Binding
The LP and LPD/BSD print spoolers were designed to use the late binding model
The data file format indications were supposed to indicate the type of file and the type of conversion needed
The use of PostScript and PCL largely eliminated this need
However, most UNIX print generation programs cannot take advantage of facilities in the printer that are well known to the user
Out of band (I.e. - information in control file) methods are used to pass this type of data, or special functions in the file generation (embedded PostScript in documents)

## Slide 136
MS Windows/MAC Use Early Binding
System configuration information records the available printers, I.e. those which have graphic to printer format converters available to the user
When printing is done, the applications program passes the data or graphical information to be displayed to the format converter which produces a file in the format appropriate to the printer
This file can be spooled or transferred directly to the printer
During printing, errors on the printing device are reported to the user via system configuration information

## Slide 137
Drivers
In the MS Windows environment, Printer drivers are actually two things
  Graphic to print file conversion programs
  print file to hardware interface programs
You can try to couple the remote printer tightly to the local host, in which case you may not be able to use printer pools or alternative printers. This is usually what is done with Microsoft Networking
You can loosely couple it by using the conversion programs, but specifying a generic printer for format purposes whose output will print on a wide variety of printers
PostScript and PCL to the rescue!

## Slide 138
Network Spooling
PC Based network printing can be loosely or tightly coupled as well
  you can either spool the entire output to a remote server
  you can wait for a connection to a printer via the print server
The print spooling method has the advantage of loosely coupling users to printers but is painfully hard to detect when an error occurs

## Slide 139
Win95 and LPR/BSD Print Spoolers
While Win95 does not directly support LPD print spooling, there are several shareware packages that provide this.
Recommended:
Windows LPR Spooler Version 4.1
Author: Susanne Heil EDV-Vertieb
ftp://ftp.astart.com/LPRng/wlprs41.exe
Implements a very good LPR/BSD RFC1179 compliant print server (LPR) and status monitor (LPQ)
Uses Winsock interface, and works with Microsoft, FTP, and several other TCP/IP Winsock.dlls

## Slide 140
Why Use Wslpr?
If you want to have a printer pool, you will be using LPRng or some other UNIX based server (unless you have big bucks)
You can also make use of the built in LPD servers in some printers
You can have a unified UNIX/Microsoft printing environment

## Slide 141
Windows NT Server LPR/BSD Gateway
Windows NT supports remote LPR printers. It will translate print jobs spooled to an NT server by creating a control file and sends the data file
Unfortunately, there are some minor problems with control file format, missing fields, etc., but these are easily handled by most LPD servers
NT also ACCEPTS print jobs for printing
This means you can use an NT server for gatewaying to the NT printer environment
Beware that there are security holes lurking in all of this

## Slide 142
Novell Printer LPD/BSD Gateways
Novell also supports a LPD/BSD gateway facility
If your Novell server has TCP/IP support installed and active, you can set up a print queue on a Novell server that will forward jobs to a LPD/BSD server.
You can also send jobs to the Novell server and it will print them

## Slide 143
Samba, SMB, and LPD/BSD Gateways
If you do not want to install Wslpr on you Win95 system, or do not want to set up an NT Server, the Samba system provides an alternative
Samba implements SMB over NetBUI and IPX
While it is usually used for file servers, Samba also supports a very nice LPD/BSD gateway facility
While not being personally familiar with the details of Samba, reports have indicated that it was trivial to set up and get working
"It worked first time, out of the box."
Kurt Reynolds

## Slide 144
PCNFS and PCNFSD Gateways to LPD
PCNFS by Sun Microsystems implements NFS (Network File System) support for PCs.
As part of this support, Sun provides source code for the PCNFSD server which is used to authenticate PCs and provide print services via the host that the server runs on.
The LPRng distribution has a set of patches for the PCNFSD distribution that interface the PCNFSD server to the LPRng print faciltities. They also close a couple of minor security problems involving unchecked string lengths and stack overflows

## Slide 145
Apple and LPR/BSD
There are several products for Apple NFS support that use the PCNFSD facilities to provide print services.
Several people have demonstrated this working very well
I would be very interested if anybody knows of a native LPD/BSD print spooler interface for the Apple TCP/IP stack

## Slide 146
Monitoring Printer Status with SNMP
One of the weak points of distributed print spooling is monitoring printers for error conditions
One of the benefits of network printers and the TCP/IP protocol is that you can query them for status from several different locations
One of the nasty problems is that most printers do not provide good status indications
The good news is that printer vendors are now implementing SNMP agents in most of their printers that allow SNMP managers to easily access printer status
The bad news is that each vendor has different extensions and facilities

## Slide 147
Perl, Tcl/TK to the Rescue?
I have seen several nice printer monitoring systems developed using Perl and Tcl/TK. Unfortunately, the most elegant ones depended on commercial SNMP managers such as OpenView and SunNetManager.
Several interested parties have been working on a simple shareware monitor; watch the LPRng ftp site for details

## Slide 148
Where Do I Get Help?
1. If it is a commercial system, try your vendors support group
2. comp.peripherals.printers news group has a large number of discussions about printers and spoolers
3. lprng@iona.ie mail list for LPRng related issues
Send mail to lprng-request@iona.ie with subscribe in the body
4. AStArt Technologies provides commercial support for LPRng and offers network consulting and management services. (Shameless plug)
Good Luck!

## Slide 149
Summary
If you are going to run printers in a multiplatform environment, you will need to deal with the issues of gateways
The LPD/BSD facilities, as defined by RFC1179, provide a common platform for use.
While by no stretch of the imagination can this be regarded as an optimal solution, it works well in an environment with a large number of printers which need central mangement and control

## Slide 150
Questions and Answers